## Slide 1: T0 and Beam Spot Calibration
Mathieu Ouillon (Mississippi State University)
07/13/26

## Slide 2: T0 Calibration
Extraction of T0 for the AHDC
First on elastic D2 run: 22990
Need to select hits on track:
  At least one hits per layer/superlayer
  p > 50MeV
  ADC > 500

## Slide 3: T0 Calibration
Extraction of T0 for the AHDC
First on elastic D2 run: 22990
Need to select hits on track:
  At least one hits per layer/superlayer
  p > 50MeV
  ADC > 500

## Slide 4: T0 Calibration
Extraction of T0 for the AHDC
Then on 4He 10.6 GeV run (22083)
Need to select hits on track:
  At least one hits per layer/superlayer
  p > 50MeV
  ADC > 500

## Slide 5: T0 Calibration
Extraction of T0 for the AHDC
Then on D2 10.6 GeV run (22598)
Need to select hits on track:
  At least one hits per layer/superlayer
  p > 50MeV
  ADC > 500

## Slide 6: T0 Calibration
To find T0:
Find the peak (5-bin method):
  Smooth the spectrum with a 5-bin moving sum (each bin replaced by the sum of itself ±2 neighbours) to suppress bin-to-bin noise.
  Take the max bin of the smoothed spectrum as the coarse peak.
Define t0: t0 = peak − 100 ns.
Fill every wire (all 576 from geometry):
  a wire with a good peak → its measured peak − 100.
  a wire with too few counts / no usable peak → the per-(SL,layer) median t0 as a fallback (no wire left blank).

## Slide 7: T0 Calibration
All T0s for 1 run (22083):

## Slide 8: T0 Calibration
Compare T0s for different runs:

## Slide 9: T0 Calibration
Compare T0s for different runs:

## Slide 10: T0 Calibration
Compare T0s for different runs:

## Slide 11: T0 Calibration
Extraction of T0 for the AHDC
On 4He 10.6 GeV run (22083)
For all hits coming from random trigger

## Slide 12: ALERT Beamspot position
Measure the transverse (𝑥, 𝑦) offset between the ALERT recoil detector and the forward- CLAS / beamline frame using coherent elastic 𝑒 + 𝑑 → 𝑒′ + 𝑑′ events.
The electron is reconstructed in forward CLAS (defining the CLAS frame); the recoil deuteron is seen in ALERT/AHDC.
For elastic kinematics the two are coplanar, so a transverse misalignment appears as a sinusoidal modulation of the azimuthal coplanarity Δ𝜑 versus the electron azimuth 𝜑𝑒.
First test it on simulation:

## Slide 13: ALERT Beamspot position
First test it on simulation:

## Slide 14: ALERT Beamspot position
And on data found (−0.75, +0.26). It is the difference between CLAS and ALERT beamspot NOT the absolute beamspot position of ALERT
For the run 22990, CLAS absolute position is
So the absolute ALERT beamspot position is